## Slide 1: Basics of using ArcGIS Pro
Research Computing Services
February 4, 2020
Dennis Milechin, P.E.
help@scc.bu.edu

## Slide 2: Outline
  Lecture
    What is GIS?
    GIS Theory
      Geographic coordinate system
      Projections
      Spatial data types
      Attributes
    ArcGIS Products
    Hands On Portion

## Slide 3: What is GIS?
  Geographic Information System
    “A geographic information system (GIS) is a system designed to capture, store, manipulate, analyze, manage, and present spatial or geographic data”
    https://en.wikipedia.org/wiki/Geographic_information_system

## Slide 4: GIS Theory – Geographic Coordinate System

## Slide 5: GIS Theory – Geographic Coordinate System
  How do I tell a computer where we are located on earth?
We are here!
(42.336046, -71.072484)

## Slide 6: GIS Theory – Geographic Coordinate System
Geographic coordinate system.
https://www.e-education.psu.edu/natureofgeoinfo/c2_p10.html
Cartesian Coordinate System
http://desktop.arcgis.com/en/arcmap/10.3/guide-books/map-projections/about-geographic-coordinate-systems.htm
http://desktop.arcgis.com/en/arcmap/10.3/guide-books/map-projections/geographic-coordinate-system.htm
http://desktop.arcgis.com/en/arcmap/10.3/guide-books/map-projections/about-geographic-coordinate-systems.htm
(50 E, 40 N)
Defined by a math model.
Point (2,2)
Notes: How much distance does a degree, minute and second cover on your maps?
The distances vary. A degree, minute or second of latitude remains fairly constant from the equator to the poles; however a degree, minute, or second of longitude can vary greatly as one approaches the poles (because of the convergence of the meridians). At 38 degrees North latitude, one degree of latitude equals approximately 364,000 ft (69 miles), one minute equals 6068 ft (1.15 miles), one-second equals 101 ft; one-degree of longitude equals 288,200 ft (54.6 miles), one minute equals 4800 ft (0.91 mile), and one second equals 80 ft.
https://www.usgs.gov/faqs/how-much-distance-does-a-degree-minute-and-second-cover-your-maps?qt-news_science_products=0#qt-news_science_products

## Slide 7: GIS Theory – Geographic Coordinate System
http://desktop.arcgis.com/en/arcmap/10.3/guide-books/map-projections/about-geographic-coordinate-systems.htm
Very complicated topic.
There are many Geographic Coordinate Systems.
There are spherical/ellipsoidal approximation of Earth.
They are updated occasionally.
North American Datum (NAD)
  NAD 27
  NAD 83 (with 5 updates)
  New Datum in 2022!
https://en.wikipedia.org/wiki/Ellipsoid

## Slide 8
http://desktop.arcgis.com/en/arcmap/10.3/guide-books/map-projections/about-geographic-coordinate-systems.htm
https://en.wikipedia.org/wiki/North_American_Datum#/media/File:Datum_Shift_Between_NAD27_and_NAD83.png
(42.336046, -71.072484)
Could be off by 40 to 45 meters!
GIS Theory – Geographic Coordinate System

## Slide 9
http://desktop.arcgis.com/en/arcmap/10.3/guide-books/map-projections/about-geographic-coordinate-systems.htm
GIS Theory –Geographic Coordinate Systems
  https://desktop.arcgis.com/en/arcmap/latest/map/projections/pdf/geographic_coordinate_systems.pdf
Geographic Coordinate Systems supported by ArcGIS Pro

## Slide 10: GIS Theory – Projections

## Slide 11: GIS Theory - Projections
What is wrong with this map?
Country | Area ( mi ^2)
Africa | 11,730,000
Antarctica | 5,405,000
Greenland | 836,300
Greenland
Antarctica
Africa

## Slide 12: GIS Theory - Projections
https://www.youtube.com/watch?v=CPQZ7NcQ6YQ
https://laughingsquid.com/world-mercator-projection-map-country-size/

## Slide 13: GIS Theory - Projections
- Allow creation of flat maps.
- At expense of distorting:
- Shape
- Area
- Direction
- Distance

## Slide 14: GIS Theory - Projections
Geographic Coordinate System
https://www.britannica.com/science/Mercator-projection/media/375638/231099
http://desktop.arcgis.com/en/arcmap/10.3/guide-books/map-projections/geographic-coordinate-system.htm
Projection

## Slide 15: GIS Theory - Projections
NAD 1983 UTM Zone 15N
Cube World
Polar NSIDC EASE Grid North
World Fuller

## Slide 16
http://desktop.arcgis.com/en/arcmap/10.3/guide-books/map-projections/about-geographic-coordinate-systems.htm
GIS Theory –Geographic Coordinate Systems
  https://desktop.arcgis.com/en/arcmap/latest/map/projections/pdf/projected_coordinate_systems.pdf
Projected Coordinate Systems supported by ArcGIS Pro

## Slide 17
http://desktop.arcgis.com/en/arcmap/10.3/guide-books/map-projections/about-geographic-coordinate-systems.htm
GIS Theory
Why do you need to care?
  Certain GIS tools require geographic coordinate system and projection to be the same for all inputs.
  Georeferencing images or old maps.
  When receiving data, like a CSV file with coordinates, make sure you know the geographic coordinate system and projection!
GIS software implements most of the GIS theory for us. Phew!

## Slide 18: GIS Theory
To learn more:
https://www.e-education.psu.edu/natureofgeoinfo/c2.html
Geographic coordinate system and projections.

## Slide 19: GIS Theory – Spatial Data Types

## Slide 20: GIS Theory – Spatial Data types
Spatial
Data Types
Vector
Raster

## Slide 21: GIS Theory – Spatial Data Types
Vector
Points
(X, Y)
Polylines
Polygon
Note: Each type of vector data is put in its own group when stored. Example, a Points Shapefile will only have points data, no polylines or polygons.

## Slide 22: GIS Theory – Spatial Data types
Spatial
Data Types
Vector
Raster

## Slide 23: GIS Theory – Spatial Data Types
Raster Data – continuous data
http://desktop.arcgis.com/en/arcmap/latest/manage-data/raster-and-images/what-is-raster-data.htm
http://desktop.arcgis.com/en/arcmap/10.3/manage-data/geodatabases/raster-basics.htm
Raster Spatial Properties
  Origin
  Cell Location
  Cell Size

## Slide 24: GIS Theory – Spatial Data Types
Examples of Raster Data
http://desktop.arcgis.com/en/arcmap/latest/manage-data/raster-and-images/what-is-raster-data.htm

## Slide 25: GIS Theory – Spatial Data Types
Spatial
Component
Vector
Raster
Points
Polylines
Polygon

## Slide 26: GIS Theory – Spatial Data Types
How is spatial data stored?
Too many options to cover in this course!
https://pro.arcgis.com/en/pro-app/help/projects/supported-data-types-and-items.htm
Common Ones:
Shapefiles
Geodatabase
CSV Files
Web Map Services

## Slide 27: GIS Theory – Attributes

## Slide 28: GIS Theory - Attributes
Spatial Component
Attribute Component
(x, y)

## Slide 29: ESRI Products

## Slide 30: ESRI – Products
Desktop Application
  ArcGIS Pro
Cloud
  ArcGIS Online
  ArcGIS StoryMaps
  ArcGIS Living Atlas
  ArcGIS Hub
  ArcGIS Apps
Enterprise Server
  ArcGIS Enterprise
Create maps for printing
Symbolize spatial data
Create, edit, delete spatial data
Toolboxes for spatial analysis
- Upload data or maps to ArcGIS Online to share
Create simple maps
Minimal spatial processing tools
Easy to share maps or spatial data
ESRI managed data repository

## Slide 31: ArcGIS Pro
Where can I get ArcGIS Pro?
Works ONLY on Windows
Alternative – QGIS (https://www.qgis.org/)
CAS IT
  Free for CAS Students, Faculty, Staff
  $125 per year for others.
  http://www.bu.edu/casit/information/purchasing-software/
Computer Labs
  CAS Building computer labs 327 and 330.
  BU Medical – “L” Building L1110

## Slide 32: ArcGIS Online
Where can I get ArcGIS Online access?
CAS IT can create an account for you
http://www.bu.edu/casit/help-request/

## Slide 33: ArcGIS Pro

## Slide 34: ArcGIS Pro – Example Workflow
Collect field data with coordinates, or download it.
https://www.mass.gov/service-details/massgis-data-layers
Clean the data
Import data into ArcGIS Pro.
Use ArcGIS Pro to visualize the data in map form.
Use Toolboxes to do spatial analysis.
Create map showing the results.
Share the map/results with others.
This Tutorial

## Slide 35: ArcGIS Pro - Resources
Introducing ArcGIS Pro
https://pro.arcgis.com/en/pro-app/get-started/introducing-arcgis-pro.htm
Help Documentation
https://pro.arcgis.com/en/pro-app/help/main/welcome-to-the-arcgis-pro-app-help.htm
ArcGIS Pro Tool Reference
https://pro.arcgis.com/en/pro-app/tool-reference/main/arcgis-pro-tool-reference.htm
ArcGIS Pro Python Reference
https://pro.arcgis.com/en/pro-app/arcpy/main/arcgis-pro-arcpy-reference.htm
Lesson Galleries of specific applications of GIS
https://learn.arcgis.com/en/gallery/

## Slide 36: Let’s Open ArcGIS Pro!